## Slide 1: A Continuous-Approximation Model to Optimize Common Stations` Density for Skip-Stop Operations
Maxime Freyss, Ricardo Giesen, Juan Carlos Muñoz
Pontificia Universidad Católica de Chile
Department of Transport Engineering and Logistics
ISTTT - July 17, 2013

## Slide 2: Outline
Motivation
Skip-stop operations
Single track skip-stop continuous approximation model
Case study and analysis of results
Conclusions

## Slide 3: Motivation – February 2007
In 2007, Santiago inaugurated a new fully integrated transit system: TRANSANTIAGO
As a result, Metro saw its demand almost double, damaging the comfort offered severely.
TRANSANTIAGO

## Slide 6: How to increase capacity?
The capacity is given by the capacity of each train and the frequency being offered
Trains could be ordered but take time to arrive
The frequency in a line for a given fleet:
f = n/tc
We needed to reduce cycle times on a network where all lines are single-tracked. Short services had already been implemented….

## Slide 8: Skip-stop operation
Skip-Stop Operation
Red station
Green station
Common station
Red station
Green station
Red station
Green station
Common station
Common station
All Stop Operation
Station 1
Station 2
Station 3
Station 4
Station 5
Station 6
Station 7
Station ..
Station 22
44 min
35 min

## Slide 9: Time-space Diagram

## Slide 10: Skip-stop operation
This idea has been implemented before few times.
  Chicago
  Philadelphia
  New York

## Slide 11: Skip-stop operation: Implementation
: Common stations
: Red stations
: Green Stations
Peak hours only
All lines except the most crowded and frequent (Line 1)

## Slide 12: Skip-stop operation: Results
Shorter travel time and lower density
Reduction in energy consumption by the lower number of traction and braking of trains
Estimated % energy savings (in regim, all day)
4 %
6 %
6 %
1 %
DENSITY

## Slide 13: Skip-stop operation: Results
Massive approval rate from users
National Innovation Award on the public Sector
But where is the research question here?

## Slide 14: Two Research questions
Provide guidelines about skip-stop operations
    When is skip-stop operation worth considering for a subway line given its characteristics (i.e. station locations, given number of trains, value of time, etc.)?
    Give general recommendations about density of common station locations (e.g. one every two, four, six stations?).

## Slide 15: Skip-stop definitions
We consider three types of stations:
  Common stations (AB) in which each train stops
  A & B stations in which half of the trains stop

## Slide 16: Continuous Approximation Model
A continuous approximation model is built assuming that local conditions surrounding a station change smoothly over the corridor.
A local function (around a station) of total costs is constructed for each operational strategy (all stop and skip-stop).
Costs are computed on [$/station/hr]

## Slide 17: Modeling Assumptions
Trains operate in a double-track circle line of length 2L, with a single track on each direction and without terminals.
Headways between trains are constant.
Maintenance costs are not considered.
No capacity constraints are considered.
Key assumption: All stations are equally likely as destination for any given trip.
Then: The maximum trip length is L and the average trip length is L/2

## Slide 18: Model Parameters
Local:
  λ [1/m]: station density in the line
  N: number of passengers starting a trip at a specific station
Global:
  L [m]: Half of total line length
  numtrains: Available trains in the fleet for each way
  a [m/s²]: Acceleration and deceleration rate of the subway
  vl [m/s]: Cruising speed of the subway
  ts [s]: Dwell time in every station
  F [N]: Traction force of a train
  VTV [CL$/s]: Social value of the travel time
  VTE [CL$/s]: Social value of the waiting time
  CE [CL$/W.s]: Energy cost
  CT [CL$]: Transfer cost

## Slide 19: Single Decision Variable
δ[/km]: Common station density
  (only for skip-stop operation)
We can solve the problem for local conditions surrounding a station and get an optimal d. This will tell us about optimal common station density around it

## Slide 20: All stop service Model
Total costs:
  All stop operation:
  Travel time + Waiting time + Operational costs
  Skip-Stop operation:
  Travel time + Waiting time + transfer time + Operational costs

## Slide 21: All stop service Model
Travel Time:
  In motion:
  Stopped:

## Slide 22: All stop service Model
Waiting Time:
  Cycle time of a train:
  Average waiting time per pax:

## Slide 23: All stop service Model
Operating Costs:
  Traction acceleration phase (very expensive) proportional to the number of stations
  Keep cruising speed between two stops (less expensive) function of the distance between stations

## Slide 24: Skip-stop Service Model
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.

## Slide 25: Example: type 1
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.

## Slide 26: Skip-stop Service Model
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.
  Type 2: From AB station to A (or B) station or vice versa. Some passengers might have to board the second stopping train.

## Slide 27: Example: type 2
We need to distinguish 5 type of trips:
  Type 2: From AB station to A (or B) station or vice versa. Some passengers might have to board the second stopping train.

## Slide 28: Skip-stop Service Model
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.
  Type 2: From AB station to A (or B) station or vice versa. Some passengers might have to board the second stopping train.
  Type 3: From A to another A station, or from B to B. Again some passengers might have to board the second passing train.

## Slide 29: Example: type 3
We need to distinguish 5 type of trips:
  Type 3: From A to another A station, or from B to B. Again some passengers might have to board the second passing train.

## Slide 30: Skip-stop Service Model
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.
  Type 2: From AB station to A (or B) station or vice versa. Some passengers might have to board the second stopping train.
  Type 3: From A to another A station, or from B to B. Again some passengers might have to board the second passing train.
  Type 4: From A station to a B station with a common (AB) station in between, or vice versa.

## Slide 31: Example: type 4
We need to distinguish 5 type of trips:
  Type 4: From A station to a B station with a common (AB) station in between, or vice versa.

## Slide 32: Skip-stop Service Model
We need to distinguish 5 type of trips:
  Type 1: From AB (common) to AB station.
  Type 2: From AB station to A (or B) station or vice versa. Some passengers might have to board the second stopping train.
  Type 3: From A to another A station, or from B to B. Again some passengers might have to board the second passing train.
  Type 4: From A station to a B station with a common (AB) station in between, or vice versa.
  Type 5: From an A to a B station without a common (AB) station in between. Passengers need to travel on the opposite direction of their destination on some leg.

## Slide 33: Example: type 5
We need to distinguish 5 type of trips:
  Type 5: From an A to a B station without a common (AB) station in between. Passengers need to travel on the opposite direction of their destination on some leg.

## Slide 34: Skip-stop Service Model
Since there are λL stations; δL common (AB) stations, and A and B stations, then the fractions of each type of trip are:

## Slide 35: Skip-stop Service Model
For types 4 and 5, the probability of trips longer than the distance to a common station is:
Then:

## Slide 36: Skip-stop Service Model
Travel time for each type can be computed based on the number of stops as a function of λ and δ for each trip type.

## Slide 37: Skip-stop Service Model
Travel Costs, waiting costs and operational Costs: Similar to all-stops service, but with different number of stops and effective frequencies per trip type.
Transfer Costs for trips type 4 and 5. An additional penalty was considered for trips type 5, since the traveler need to change platform (and direction)

## Slide 38: Case Study
Since we could not find an analytical expression for the optimal density of common stations on skip-stop operations
A numerical analysis was performed, and assuming typical values for the system parameters

## Slide 39: Case Study
L=10.000m = 10 Km
fleet=25 trains
N=5000 pax/hr
λ=1 station every 500 meters

## Slide 40: Analysis of results
Effect of each variable on the objective function
Sensitivity analysis of global parameters
Sensitivity analysis of local parameters

## Slide 41: Effect of different parameters in the Objective Function
Waiting times decrease when δ increases
Transfer costs decrease when δ increases
Travel time decrease and then increase with δ
Operational costs increase when δ increases

## Slide 42: Effect of each term on the objective function

## Slide 43: Sensitivity analysis on fleet size
Skip-stop operations are less convenient with lower frequencies
Examples: regional trains, off-peak periods
Optimal density is robust to changes in station density

## Slide 44: Sensitivity analysis on line (trip) length
Gains are higher when L is longer
Optimal density is smaller
Thus, skip-stop operations are more convenient when trips are longer.

## Slide 45: Sensitivity analysis on value of time
The optimal density of common stations varies only a little

## Slide 46: Sensitivity analysis on the volume of passengers
For Chilean value of time or higher, pax volumes have small influence
For smaller values of time is more relevant

## Slide 47: Sensitivity analysis on density of existing stations
Skip-stop is more convenient when station density is high

## Slide 48: Conclusions
The model identifies skip-stop operation attractiveness given easily accessible information
Skip-stop operations are not advisable for systems with: low frequency, low average trip length, or low density of stations.
The proposed model can be used to find the optimal density of common stations.
The optimal density of common stations is quite stable with respect to the parameters studied.

## Slide 49: Conclusions/Observations
Skip-Stop can reduce social costs significantly
It can also increase capacity improving comfort
Demand in the corridor adapts to skip-stop operations; transferring trips drop significantly
Implement first the less busy direction only

## Slide 50: A Continuous-Approximation Model to Optimize Common Stations` Density for Skip-Stop Operations
Maxime Freyss, Ricardo Giesen, Juan Carlos Muñoz
Pontificia Universidad Católica de Chile
Department of Transport Engineering and Logistics
ISTTT - July 17, 2013

## Slide 51: Benefits of increased travel speed
Reduce cycle times
Reduce number of vehicles
Reduce headways
Reduce operating costs
Increase profits or reduce subsidies
Reduce Travel times
Reduce Waiting times
Increase in modal share (pax diverted from automobile)
Operational alternatives
Benefits
Increase capacity
Improve comfort

## Slide 52: Análisis de sensibilidad (evaluación social)
De nuevo, el óptimo es muy estable
Sin embargo impacta la segunda parte de las curvas
Por eso ayuda a entender que lo que realmente define el óptimo es el tiempo de viaje (ver siguiente)

## Slide 53: Influencia de la variable en la FO
Tiempo de viaje:

## Slide 54: Skip-stop Service Model
Waiting Time: Similar to all stop but with different cycle time:
Trip type 1:
Ese tiempo representa la « unidad temporal »

## Slide 55: Modelación del servicio expreso
Types 2 and 3:
Promedio: 2 « unidades » de espera
1
2
1
Or
Trenes A
Trenes B
Posición temporal del pasajero
1 Unidad de tiempo

## Slide 56: Modelación del servicio expreso
Tipos 4 y 5:
Promedio: 4 « unidades » de espera

## Slide 57: Aparte sobre los headways
Se tiene que ajustar la flota en función del largo de la línea para que la frecuencia:
  No sea demasiado baja (los tiempos de espera subirían mucho)
  No sea demasiado alta para respetar el mínimo técnico headway (no tiene que superar 90 segundos)

## Slide 58: Contenidos
Contexto y Motivación
Funcionamiento de servicio expreso
Modelación de una línea ferroviaria
Análisis de resultados
Relajación de los supuestos
Conclusiones

## Slide 59: Base del trabajo
El operador debe elegir entre aumentar frecuencia (con la misma flota) y reducir la flota
Lo que se hace en Santiago hoy día: aumentar frecuencia
El punto de vista es más « social ». Se eligió trabajar con ese.

## Slide 60: Contenidos
Contexto y Motivación
Funcionamiento de servicio expreso
Modelación de una línea ferroviaria
Análisis de resultados
Relajación de los supuestos
Conclusiones

## Slide 61: « Cada estación es equiprobable »
Situación real e impactos:
  Función de distribución de largos de viaje
  Viajes muy cortos (tipo 5) muy pocos probables en realidad
  Supuesto castiga mucho skip-stop
Como se podría resolver:
  Considerar la función de distribución de verdad
  Encontrar los Pi con simulación

## Slide 62: « No hay problemas de capacidad »
Situación real e impactos:
  Hay estaciones donde todos los pasajeros no pueden subirse al primer tren que llega
  Implica un gran costo en tiempo de espera adicional
  El modelo tendría que indicar que las estaciones AB sean las con mayor demanda
Como se podría resolver:
  Considerar capacidad con procesos de llegada de los pasajeros a las estaciones y tomar en cuenta los niveles de ocupación de los trenes