## Slide 1: The evening commute with cars and transit: Duality results and user equilibrium for the combined morning and evening peaks
20th International Symposium on Transportation and Traffic Theory
18 July 2013, Noordwijk, the Netherlands
Eric J. Gonzales
Assistant Professor
Civil and Environmental Engineering
Rutgers University
Carlos F. Daganzo
Robert Horonjeff Professor
Civil and Environmental Engineering
University of California, Berkeley

## Slide 2: Research Problem
To plan for and manage congested transportation systems, we need to understand how people will use the system.
in the evening rush?
when considering their round-trip commute?
How do people choose when to travel and which mode to use

## Slide 3: Research Problem
Models of congestion and mode use should
To plan for and manage congested transportation systems, we need to understand how people will use the system.
in the evening rush?
when considering their round-trip commute?
be consistent with physics and dynamics of queueing.
consider bottlenecks and transit systems with capacity constraints.
address daily schedule preferences.
How do people choose when to travel and which mode to use

## Slide 4: Literature
Extensive work has been done on the morning commute problem,
(Vickrey 1969; Smith 1984; Daganzo 1985; Arnott, de Palma, Lindsey 1990; et al.)
including models that consider mode choice.
(Tabuchi 1993; Braid 1996; Huang 2000; Danielis, Marcucci 2002; Qian, Zhang 2011; Gonzales, Daganzo 2012)
Few studies have considered the evening commute, and they have done so for cars only.
(Vickrey 1973; Fargier 1981; de Palma, Lindsey 2002)
Models of daily bottleneck travel decisions have relied on linking morning and evening by work duration
(Zhang, Yang, Huang, Zhang 2005)
or parking availability.
(Zhang, Huang, Zhang 2008)

## Slide 5: Overview
User Equilibrium for Morning with Transit
User Equilibrium for Evening with Transit
1
2
System Optimum for Isolated Morning, Evening
3
User Equilibrium for Combined Morning & Evening
4
Independent Morning and Evening Preferences
Rigid Work Duration with Flexible Start Time
Fixed Wished Order with Cars and Transit

## Slide 6: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
ORIGIN
(Home)
DESTINATION
(Work)
BOTTLENECK
Given:
TRANSIT
capacity for cars
capacity for cars and transit
commuters with cumulative wished departures,

## Slide 7: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
ORIGIN
(Home)
DESTINATION
(Work)
BOTTLENECK
Given:
TRANSIT
capacity for cars
capacity for cars and transit
commuters with cumulative wished departures,
generalized cost of uncongested car trip
generalized cost of uncongested transit trip
Mode Costs
difference of mode costs

## Slide 8: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
ORIGIN
(Home)
DESTINATION
(Work)
BOTTLENECK
Given:
TRANSIT
capacity for cars
capacity for cars and transit
commuters with cumulative wished departures,
generalized cost of uncongested car trip
generalized cost of uncongested transit trip
Mode Costs
difference of mode costs
Schedule Preference relative to departure
units of equivalent queuing time
Penalty
Schedule Deviation

## Slide 9: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
In equilibrium, users choose when to travel and which mode to take in order to minimize the generalized cost of their own trip:
Cost = Uncongested Mode Cost + Queueing Delay + Schedule Penalty
Time
Cum. Trips
(# trips)
EARLY
LATE
Equilibrium arrival curve and departure curve leaves no incentive to change departure time.

## Slide 10: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
In equilibrium, users choose when to travel and which mode to take in order to minimize the generalized cost of their own trip:
Cost = Uncongested Mode Cost + Queueing Delay + Schedule Penalty
Slope of equilibrium arrival curve must satisfy:
early departure, only cars
early departure, cars and transit
late departure, cars and transit
late departure, only cars

## Slide 11: Morning Commute, Cars and Transit
USER EQUILIBRIUM: MORNING WITH TRANSIT
Time
Cum. Trips
(# trips)
EARLY
LATE
Commuters use only car at beginning and end of rush, when queueing delay is less than .
In the middle of the rush, both modes are used.

## Slide 12: Evening Commute, Cars and Transit
USER EQUILIBRIUM: EVENING WITH TRANSIT
DESTINATION
(Home)
ORIGIN
(Work)
BOTTLENECK
Given:
TRANSIT
capacity for cars
capacity for cars and transit
commuters with cumulative wished departures,
generalized cost of uncongested car trip
generalized cost of uncongested transit trip
Mode Costs
difference of mode costs
Schedule Preference relative to arrival
units of equivalent queuing time
Penalty
Schedule Deviation

## Slide 13: Evening Commute, Cars and Transit
USER EQUILIBRIUM: EVENING WITH TRANSIT
In equilibrium, users choose when to travel and which mode to take in order to minimize the generalized cost of their own trip:
Cost = Uncongested Mode Cost + Queueing Delay + Schedule Penalty
Time
Cum. Trips
(# trips)
EARLY
LATE
Equilibrium arrival curve and departure curve leaves no incentive to change arrival time.

## Slide 14: Evening Commute, Cars and Transit
USER EQUILIBRIUM: EVENING WITH TRANSIT
In equilibrium, users choose when to travel and which mode to take in order to minimize the generalized cost of their own trip:
Cost = Uncongested Mode Cost + Queueing Delay + Schedule Penalty
Slope of equilibrium arrival curve must satisfy:
early arrival, only cars
early arrival, cars and transit
late arrival, cars and transit
late arrival, only cars

## Slide 15: Evening Commute, Cars and Transit
USER EQUILIBRIUM: EVENING WITH TRANSIT
Time
Cum. Trips
(# trips)
N
EARLY
LATE
Like the morning, commuters use transit only when queues exceed .

## Slide 16: Comparison: Morning and Evening Equilibrium
ISOLATED MORNING AND EVENING COMMUTES
Morning
Evening
Ratio of Early/Late Commuters

## Slide 17: Comparison: Morning and Evening Equilibrium
ISOLATED MORNING AND EVENING COMMUTES
Morning
Evening
Ratio of Early/Late Commuters
Number Traveling at rate
Maximum Travel Cost,
Number Traveling at rate

## Slide 18: System Optimum
ISOLATED MORNING AND EVENING COMMUTES
Optimal use of the bottlenecks should involve no queueing. Arrival and departure curves should be the same.
The morning and evening schedule penalty is measured relative to the same curve, so the system optimum takes the same form in both cases.
Time
Cum. Trips
(# trips)
or
or
or

## Slide 19: System Optimum
ISOLATED MORNING AND EVENING COMMUTES
Optimal use of the bottlenecks should involve no queueing. Arrival and departure curves should be the same.
The morning and evening schedule penalty is measured relative to the same curve, so the system optimum takes the same form in both cases.
Time
Cum. Trips
(# trips)
or
or
or
Optimal prices must increase at rate or for early travelers, and decrease at rate or for late travelers.

## Slide 20: User Equilibrium for the Round-trip Commute
COMBINED MORNING AND EVENING COMMUTES
Commuters consider both their morning and evening commutes when making travel choices.
Schedule Penalty is a function of morning and evening:
HOME
WORK
EVENING
BOTTLENECK
capacity
departure time in morning
identical commuters
MORNING BOTTLENECK
capacity
arrival time in evening

## Slide 21: Existence of Combined Equilibrium
COMBINED MORNING AND EVENING COMMUTES
Proposition 1
If is a positive definite, twice differentiable function with partial derivatives such that
then a user equilibrium exists for the combined morning and evening peaks in which the commuters depart in the same first-in-first-out (FIFO) order in both peaks.
Notes: First: earliness in the morning is less costly than queuing
Second: lateness in the evening is less costly than queuing
Third: Required for preserved FIFO order in both rushes
Penalties functions include broad cases:
Separable functions of the morning departure and the evening arrival times
Function of work duration (the difference between evening arrival and morning departure)
Linear combinations of these two
Bilinear schedule penalties of the type introduced previously

## Slide 22: Existence of Combined Equilibrium
COMBINED MORNING AND EVENING COMMUTES
Proposition 1
This includes a broad range of schedule penalty functions including:
If is a positive definite, twice differentiable function with partial derivatives such that
then a user equilibrium exists for the combined morning and evening peaks in which the commuters depart in the same first-in-first-out (FIFO) order in both peaks.
separable penalty function
function of work duration
Notes: First: earliness in the morning is less costly than queuing
Second: lateness in the evening is less costly than queuing
Third: Required for preserved FIFO order in both rushes
Penalties functions include broad cases:
Separable functions of the morning departure and the evening arrival times
Function of work duration (the difference between evening arrival and morning departure)
Linear combinations of these two
Bilinear schedule penalties of the type introduced previously

## Slide 23: Independent AM and PM Schedule Preferences
COMBINED MORNING AND EVENING COMMUTES
Schedule penalty is the sum of two independent functions:
User equilibrium is the same as solving morning and evening independently.
For bilinear schedule preferences:
for early commuters
for late commuters
for early commuters
for late commuters
Notes: Note that in general there will not be the same number of early and late travelers in both peaks.

## Slide 24: Rigid Work Duration
COMBINED MORNING AND EVENING COMMUTES
Schedule requires work duration , with flexible start and end time.
For bilinear schedule preferences, such that and :
for early commuters
for late commuters
for
otherwise

## Slide 25: Rigid Work Duration
COMBINED MORNING AND EVENING COMMUTES
Time
Cum. Trips
(# trips)
EARLY
LATE

## Slide 26: Fixed Wish Order with Cars and Transit
COMBINED MORNING AND EVENING COMMUTES
Mode choice can easily be reintroduced in the case that wished order for morning departure and evening arrivals are the same.
Transit is competitive for commuters facing round-trip queuing of .

## Slide 27: Fixed Wish Order with Cars and Transit
COMBINED MORNING AND EVENING COMMUTES
Mode choice can easily be reintroduced in the case that wished order for morning departure and evening arrivals are the same.
For the case that demand rates are and , and transit capacity is proportional to and :
Transit is competitive for commuters facing round-trip queuing of .
Number of early drivers, before transit is used
Number of late drivers, after transit is used

## Slide 28: Fixed Wish Order with Cars and Transit
COMBINED MORNING AND EVENING COMMUTES
Time
Cum. Trips
(# trips)
CAR ONLY
CAR ONLY
CAR & TRANSIT

## Slide 29: Fixed Wish Order with Cars and Transit
COMBINED MORNING AND EVENING COMMUTES
Proposition 2
If commuters travel in the combined morning and evening commute with common wished order, there there are at least as many transit riders in the combined user equilibrium as there are in the isolated morning and evening commutes together.

## Slide 30: Findings
For identical travelers, a broad set of schedule penalties result in a combined user equilibrium in commuters travel in the same FIFO order in both rushes.
The evening user equilibrium is not simply the reverse of the morning user equilibrium.
System optimum for an isolated rush takes the same form for morning and evening commutes.
Combined user equilibrium with transit is well defined when the wished order is the same in the morning and evening. This condition is favorable for transit.

## Slide 31
Thank You
Eric J. Gonzales
Civil and Environmental Engineering Rutgers, The State University of New Jersey
eric.gonzales@rutgers.edu
Notes: I make use of a macroscopic relationship between the average flow of vehicles on a network and the density of vehicles per distance on that network, which we call the Macroscopic Fundamental Diagram (or MFD). The advantage of this aggregate method for modeling cities is that we do not need detailed information about the demand and traffic conditions on every street, so with fewer data inputs we can reliably predict the network’s aggregate performance.
Here, I show an idealized MFD, and the intuition is as follows:
At low vehicle densities, roads are empty so vehicles move quickly but flows are low;
As the number of vehicles in the network increases, flows too increase up to a point;
Then queues of cars begin to block each other and impede flow as the network becomes congested and flows drop.
What is important about the MFD is that it is a property of the network. Even as demand patterns change, the maximum flow consistently corresponds to the same critical vehicle density.