## Slide 1: Longitudinal Driving Behavior in case of Emergency situations: An Empirically Underpinned Theoretical Framework
Dr. R.(Raymond) G. Hoogendoorn, Prof. dr. ir. B. (Bart) van Arem and Prof. dr. K. (Karel) A. Brookhuis

## Slide 2: Outline
Introduction;
State-of-the-art:
  Empirical longitudinal driving behavior in case of an emergency;
  Mathematical modelling of driving behavior in case of an emergency;
Introducing a theoretical framework of behavioural adaptation;
Research method;
Results;
Conclusion;

## Slide 3
1.
Introduction

## Slide 4: Introduction
The ability of transport systems to deal with adverse conditions is becoming increasingly important;
Major impact on traffic flow operations;
Georges (1998) and Floyd (1999) led to enormous traffic jams;
Little experience is on how to cope with them;
In order to evaluate measures, simulation studies must be performed;
Mathematical models of driving behavior (car-following, lane changing);
Important to gain insight into:
  Empirical adaptation effects in driving behavior;
  Representation of these effects in mathematical models;

## Slide 5: Introduction2
Determinants of driving behavior?
Provides us with indications on how to best model this behavior;
New theoretical framework of longitudinal driving behavior in case of emergency situations;
Task-Capability-Interface model by Fuller (2005);
Compensation and performance effects in driving behavior;
However, it is not yet clear:
  To what extent these effects can be found in empirical driving behavior;
  To what extent these effects are represented in mathematical car-following models;
Empirical underpinning of the framework;

## Slide 6
2.
State-of-the-art

## Slide 7: Empirical longitudinal driving behavior in case of an emergency
Tu et al. (2010): anxious behavior due to a mentally demanding situation;
Hamdar and Mahmassani (2008):
  Increase in speed;
  A high variance in speed;
  A reduction in spacing to force others to accelerate or move out of the way;
  An increase in emergency braking;
  An increase in intensity with regard to speed and braking rates over time;

## Slide 8: Mathematical modeling of driving behavior
Several mathematical models have been developed aimed at mimicking driving behavior under a wide range of conditions;
General form:
Each model has its own control objective (for instance safe-distance models; Gipps (1981));
But also, the Intelligent Driver Model (Treiber et al., 2000):

## Slide 9: Mathematical modeling of driving behavior2
Drawbacks of these models:
  Only the behavior of the direct lead vehicle is a stimulus;
  The only human element is a finite reaction time, other human elements are quite mechanistic;
  Drivers are assumed to react to lead vehicle related stimuli, no matter how small;
  Drivers are assumed to perceive stimuli, no matter how small;
  Situations are adequately evaluated and responded to;
  The gas and brake pedal are operated in a precise manner;
  Drivers are, in reality, not permanently engaged in the driving task;
Leutzbach and Wiedemann (1986): psycho-spacing models;

## Slide 10: Mathematical modeling of driving behavior3
Approaching at a constant relative speed;
On crossing the thresholds, the driver will change his behavior;
Action point;
Typical spiralling behavior observed from data;
Changes in accelerations typically in the order of 0.2 m/s2;

## Slide 11: Mathematical modeling and emergencies
Hamdar & Mahmassani (2008): capturing driving behavior under extreme conditions through an adaptation of the Gipps model (Gipps,1981);
Application of higher acceleration rates;
Alteration of the variable representing desired speed;
Tampere (2004): inclusion of activation level into a model of driving behavior;
But what about a theoretical framework of these changes in behavior?

## Slide 12
3.
Introducing a theoretical framework

## Slide 13: Introducing a theoretical framework
In the Task-Capability-Interface model (Fuller, 2005) task difficulty comes forth from the dynamic interaction between:
  Task demands;
  Driver capability;
Driver capabilities are restricted by biological personal characteristics of drivers as well as by experience;
But also dynamic determinants:
  Activation level (see also Tampere, 2004);
  Distraction;
Task demands:
  Adverse weather;
  Road design;
  Etc.

## Slide 14: Introducing a theoretical framework2
Most important: elements in the task over which the driver has direct control (e.g., speed);
Compensation effects;
Therefore interaction between task demands and driver capability;
In case of an emergency it may be assumed that driver capability increases due to an increase in activation level;
Perhaps also an influence on task demands, e.g., visibility, traffic intensity, etc.;
When driver fail the task due to an imbalance, performance effects are the result, e.g., increase in reaction time, reduction in the adequacy of the car-following task;

## Slide 15: Introducing a theoretical framework4
Most important: elements in the task over which the driver has direct control (e.g., speed);
Compensation effects;
Therefore interaction between task demands and driver capability;
In case of an emergency it may be assumed that driver capability increases due to an increase in activation level;
Perhaps also an influence on task demands, e.g., visibility, traffic intensity, etc.;
When driver fail a task due to an imbalance, performance effects are the result, e.g., increase in reaction time, reduction in the adequacy of the car-following task;
However, no empirical underpinning was available;

## Slide 16: Introducing a theoretical framework3

## Slide 17
4.
Research method

## Slide 18: Research method
Research questions:
  To what extent do emergency situations influence empirical longitudinal driving behavior?
  To what extent are compensation effects reflected in parameter value changes of continuous car-following models?
  To what extent are performance effects reflected in model performance of continuous car-following models?
  To what extent are compensation effects reflected in position of action points in psycho-spacing models?
  To what extent are performance effects reflected sensitivity towards lead vehicle related stimuli at these action points?

## Slide 19: Research method2
Driving simulator experiment;
Complete multi-factorial design;
Between as well as within subject factors;
Control group (no urgency) and experimental group (urgency);
Monetary reward when reaching destination in time (max EUR 20,-);
Three within subject conditions:
  On Time
  Behind schedule;
  Out of Time;

## Slide 20: Research method3

## Slide 21: Research method5
Longitudinal driving behavior is measured at 10Hz;
38 employees and participants of Delft University of Technology;
21 male and 17 female participants;
Age varied from 21 to 56 years (Mean=30.41, SD=5.30);
Driving experience varied from 3 to 29 years (Mean=10.31, SD=6.41);
MANOVA’s
Estimation of parameters of the Intelligent Driver Model (Treiber et al., 2000) through the method described in Hoogendoorn and Hoogendoorn (2010);
Estimation of action points in the relative speed – spacing plane through the method proposed in Hoogendoorn et al. (2011);
Curve fitting of perceptual thresholds;

## Slide 22: Research method6
Multivariate Regression Analysis using the following model:

## Slide 23
5.
Results

## Slide 24: Empirical adaptation effects
Results Multivariate Analysis of Variance;
Significant main effects and interaction effects;
Significant increase in speed and acceleration;
Significant reduction in spacing;
Significant reduction in relative speed;
Variable | Factor | Pillai’s T | F | d f | Error | p
Speed v | Urgency(2) | - | 39.53 | 1 | 38 | .00
 | Time(3) | .29 | 8.30 | 2 | 76 | .00
 | Urgency(2) x Time(3) | .34 | 10.39 | 2 | 76 | .00
Acceleration a | Urgency(2) | - | 5.24 | 1 | 38 | .02
 | Time(3) | .06 | 1.48 | 2 | 76 | .23
 | Urgency(2) x Time(3) | .07 | 1.74 | 2 | 76 | .18
Deceleration b | Urgency(2) | - | 1.63 | 1 | 38 | .24
 | Time(3) | .05 | .99 | 2 | 76 | .37
 | Urgency(2) x Time(3) | .02 | .32 | 2 | 76 | .72
Spacing s | Urgency(2) | - | 34.94 | 1 | 38 | .00
 | Time(3) | .33 | 9.41 | 2 | 76 | .00
 | Urgency(2) x Time(3) | .29 | 12.94 | 2 | 76 | .00
Positive relspeed ∆vpos | Urgency(2) | - | 17.80 | 1 | 38 | .00
 | Time(3) | .22 | 6.19 | 2 | 76 | .00
 | Urgency(2) x Time(3) | .23 | 6.20 | 2 | 76 | .00
Negative relspeed ∆vneg | Urgency(2) | - | 9.02 | 1 | 38 | .00
 | Time(3) | .16 | 4.12 | 2 | 76 | .00
 | Urgency(2) x Time(3) | .14 | 5.11 | 2 | 76 | .00

## Slide 25: Compensation effects – Parameter values of the IDM
Substantial changes in the parameter values of the Intelligent Driver Model;
Increase in max acceleration and deceleration;
Increase in free speed;
Reduction in desired time headway;
Indication for compensation effects in driving behavior;
Parameter | Mean | Std | Min | Max
Control group Maximum acceleration a (m/s2 ) | 0.94 | 0.68 | 0.35 | 2.03
Maximum deceleration b (m/s2 ) | 0.87 | 0.34 | 0.57 | 1.18
Free speed v0 (m/s) | 29.97 | 4.02 | 25.87 | 34.01
Desired time headway T (s) | 0.78 | 1.06 | 0.07 | 2.99
Experimental group Maximum acceleration a (m/s2 ) | 1.46 | 0.65 | 0.80 | 2.14
Maximum deceleration b (m/s2 ) | 0.97 | 0.21 | 0.70 | 1.18
Free speed v0 (m/s) | 35.27 | 3.07 | 32.38 | 39.51
Desired time headway T (s) | 0.25 | 0.68 | 0.09 | 0.45

## Slide 26: Compensation effects – Parameter values of the IDM2

## Slide 27: Compensation effects – Parameter values of the IDM3

## Slide 28: Compensation effects – Parameter values of the IDM4

## Slide 29: Compensation effects – Parameter values of the IDM5

## Slide 30: Performance effects – Model performance of the IDM
Comparison with null model;
Model assuming zero acceleration;
Significant reduction in model performance in case of the emergency situation;
The behavior of the lead vehicle less adequately describes the behavior of the follower; performance effects

## Slide 31: Compensation effects – Action points and perceptual thresholds
Overlap in acceleration increases and reductions;
However, strong bias;
Substantial difference in the position of action points between the two groups;
Less scatter; more action points at smaller values of spacing;

## Slide 32: Compensation effects – Action points and perceptual thresholds2
Reflected in the shape of the perceptual thresholds;
Indication for compensation effects in driving behavior;

## Slide 33: Performance effects – Sensitivity acceleration at action points
Reduction in the sensitivity of acceleration towards relative speed and spacing;
Increase in the error and MSE;
Indication for performance effects;

## Slide 34
6.
Conclusion and Discussion

## Slide 35: Conclusion
Emergency situations have a substantial impact on driving behavior;
Theoretical framework: interaction between task demands and driver capability leads to compensation and performance effects;
Indication for compensation effects:
  Parameter value changes in the IDM
  Changes in the shape and position of perceptual thresholds;
Indication for performance effects:
  Model performance of the IDM;
  Reduction in sensitivity of acceleration towards lead vehicle related stimuli at action points;

## Slide 36: Discussion
Indication for the existence of compensation and performance effects in driving behavior;
First step towards the empirical underpinning of the theoretical framework;
However:
  More insight into task demands and driver capability is needed;
  What is the influence of static and dynamic driver characteristics;
  What is the influence of an emergency situation on task demands?
The results are mere indications of compensation and performance effects;
Adequate measures of these effects have to be developed;
Furthermore, driving simulator data was used, validity issues!
Relative small sample size;

## Slide 37
Thank you for your attention!