## Slide 1: A transportation programming model considering project interdependency and regional balance
<number>
The 20th International Symposium on Transportation and Traffic Theory
Noordwijk, the Netherlands
July 18, 2013
Kuancheng Huang* and Yi-Ming Kuo
Dept. of Transportation and Logistics Management National Chiao Tung University, Taiwan

## Slide 2: Outlines
<number>
Introduction
Problem Background and Literature Review
Mathematical Model
Solution Algorithm
Conclusions

## Slide 3: Transportation Programming (TP)
<number>
Introduction
Given a fixed budget, how to select the projects to be implemented?
25 transportation projects in Taiwan with a cost larger than 1 billion NTD in 2010

## Slide 4: Knapsack Problem (KP) Approach
<number>
-bj (benefit of project j)
G (budget)
mj (cost of project j)
Issue I: Project Inter-dependency
Issue II: Regional Balance
Introduction

## Slide 5: Example of Political Influence
The districts receiving the most funds are … (Spanish data for the period 1964–2004)
  The incumbent’s vote margin is low.
  Few votes are needed to win an additional seat.
  The central and regional governments are controlled by the same party.
  Regional parties play a pivotal role in the legislature.
<number>
Solé-Ollé, A. (2013), Inter-regional redistribution through infrastructure
investment: tactical or programmatic, Public Choice, 156:229–252.
Literature Review & Background

## Slide 6: TP Works w/ Dependent Projects
<number>
Literature Review & Background
Complementary
Substitutive
Teng & Tzeng (1996), A multiobjective programming approach for selecting non-independent transportation investment alternatives, TR-B, 30: 291-307.
Independent

## Slide 7: Iniestra and Gutiérrez (2009)
Follow the multi-objective context and project-interdependent features
  The average benefit/cost ratio of project portfolio
  The relevance to network connectivity
  State authorities’ preferences (an assigned importance rank)
  The total level of congestion in the region
  The social impact (# of people who benefit)
Solve the problem by Genetic Algorithm
<number>
Literature Review & Background
Li et al. (2012), New Methodology for Transportation Investment Decisions with Consideration of Project Interdependencies, TRR, 2285:36-46.

## Slide 8: Modeling Inter-dependency
<number>
Basic project
Joint project: the overall benefit (or cost) is different from the sum of the individual benefits (or costs) of the basic projects.
x1
x2
x3
x1
x2
Literature Review & Background

## Slide 9: Other Exclusive Relations
<number>
“Intrinsic” exclusive relations (beyond the issue of joint projects)
  For one single initiative, the various versions (e.g., a one-lane or two-lane expansion of a highway section).
  For multiple initiatives, the corresponding options (e.g., a public bus terminal vs. a commuter parking facility) cannot be selected simultaneously (e.g., utilizing the same piece of land).
Literature Review & Background

## Slide 10: Integer Programming Model
<number>
s.t.
Mathematical Model
Minimize negative benefit (Maximize benefit)
Budget constraint
Exclusive Relations, e.g.,
Regional balance: project j contributes aij to region i.
A modification to SCP (Set Covering Problem)
λi
π
to be relaxed

## Slide 11: Significance (Relevance) Level
<number>
A 51.03-km MRT line (140 billion NTD) connecting Taipei city center and the major int’l airport
Capital City
Economic Center
0.25
Heavily Populated Suburban
0.75
Industry
Airport (Aerotropolis)
1.00

## Slide 12: Lagrangian Relaxed Model
<number>
Exclusive Relations, e.g.,
Constraints similar to those of the classic assignment problem (AP), which holds the Total Uni-modularity property.
Linearly relax the LR problem.
Mathematical Model

## Slide 13
<number>
Solution Algorithm
Flowchart of Algorithm

## Slide 14: Feasible Solution
<number>
STEP 1: If the significance constraint (5) is violated, add the unselected option based on the Lagrangian cost cj(, π) in “ascending” order until Constraint (5) is satisfied.
STEP 2: If the budget constraint (6) is violated, remove the selected options (a) based on the Lagrangian cost cj(, π) in “descending” order and (b) under the condition of satisfying Constraint (5), until the overall budget is under the limit.
STEP 3: If there is a slack for Constraint (6), further add the option with the most negative Lagrangian cost cj(, π) until the budget is fully utilized.
Note: For STEP 1 and STEP 3, an option is added only if the mutually exclusive constraint (7) is not violated.
Mathematical Model

## Slide 15: Lagrangian Multiplier Update
<number>
Sub-gradient Method (Held & Karp, 1970)
Mathematical Model

## Slide 16: Illustrative Example
<number>
Numerical Experiment
Imposing coverage constraint
Benefit maximization only
International Airport MRT System
International Airport RWY #1 Improvement
National Freeway #4 Extension
National Freeway #6 Extension
Highway #9 Phase III Improvement
Highway #11 Pacific Coast Highway Improvement
National Freeway #6 Extension
Local Railway MRT Transformation (Section I)
Local Railway MRT Transformation (Section IV)
West Coast Highway Improvement
Highway #.9 Mountain Section Improvement
Chiayi City Local Railway Overheadization

## Slide 17: Results of the Illustrative Example
<number>
Numerical Experiment
Price for compromising!

## Slide 18: Hypothetical Test Problems
<number>
Numerical Experiment
Significance Level Setting
Project Inter-dependence

## Slide 19: Results of Hypothetical Problems
<number>
Numerical Experiment
30 test problems of each problem scale

## Slide 20: Conclusions
<number>
An IP model addressing two practical TP features: project interdependency and regional balance.
  Two Things You Shouldn't Watch Being Made: Sausage and Legislation (Mark Twain)
A Lagrangian-relaxed solution algorithm to derive a promising approximate solution and a tight bound .
Future Research Extensions
  A multi-stage model to address the issue of consistency
  A stochastic model for the issue of uncertainty
  A multi-objective model, given the diversified stakeholders
Conclusions