## Slide 1: On Joint Railway and Housing Development Strategy
Xiaosu Ma 1 and Hong K. Lo 2
1 Singapore-MIT Alliance for Research and Technology
2 The Hong Kong University of Science and Technology (cehklo@ust.hk)

## Slide 2: Background
Transit Oriented Development (TOD)
  Efficient, reliable, environmentally friendly, extensively pursued in Asia, especially China
  One critical issue is financial sustainability of rail development
  The question is to what extent one can exploit the synergy between rail and property developments
    Property development brings in rail patronage, hence higher fare revenue
    Improved accessibility due to rail increases values of properties
    To what extent property value increases can be used to cross-subsidize rail infrastructure development

## Slide 3: Background
Empirical studies
  Property values increase in areas near quality transit stations (Hass-Klau et al., 2004; Rodriguez and Targa, 2004; Munoz-Raskin, 2007).
MTRC in Hong Kong
  Granted right to develop properties above MTR stations,
  Profit from property development cross-subsidizes rail infrastructure investment
  50% revenue from rail, property development contributes 90% profit (MTRC, 2010)

## Slide 4: Background
Past efforts focus on value capture and investment models (Lo et al., 2008; Tang and Lo, 2008, 2010)
  Statistical approaches relate railway development and property value for individual sites
  State-of-the-art land-use and transport models are used to study TOD through simulation methods.
  Few focused on developing an analytical framework via a combined equilibrium formulation and deriving analytical results

## Slide 5: Objective
To study the impact of joint railway and property development strategies on the system performance and benefit distribution among stakeholders.

## Slide 6: Outlines
The modeling framework
Properties and sensitivity tests
Numerical example
Conclusion

## Slide 7: The modeling framework
1.

## Slide 8: The modeling framework
Lower level
Upper level
1
Residents
TOD developer

## Slide 9: The combined equilibrium formulation
To model heterogeneous residents’ location and travel choices
  With given transport network and housing supply
1.1
Housing market
Bid rent process

## Slide 10: The combined equilibrium formulation
Formulated as an equivalent Nonlinear Complementarity Problem (NCP)
Lower level decision variables - Z
  Utility level index
  Rail demand
  Auto path flow
Further reformulated as an unconstrained optimization problem by minimizing a gap function to zero
1.1
Travel choice
Location choice

## Slide 11: Joint railway and housing development
The upper level story
  A profit oriented joint railway and housing developer
  Upper level decision variables
    Railway service (headway and fare)
    Housing supply (housing type and number)
  With exogenous total demand
  With other competitive travel modes, e.g. auto
1.2
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 12: Joint railway and housing development
Profit function
1.2
Housing revenue
Rail revenue
Housing cost
Rail cost
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 13: Joint railway and property development
Mathematical Program with Equilibrium Constraints (MPEC)
1.2
s.t.
Gap function for the combined equilibrium
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 14: Properties and sensitivity tests
2.
Notes: With the above formulation which combines both residents’ and developers’ decision making process, it is of interest to analyze the resultant benefit redistribution among them due to different railway and housing investment strategies, such as changes in resident consumer surplus, railway and housing developer’ producer surplus, as well as the overall social welfare.

## Slide 15: Properties
2
Results obtained for the case of
  One OD, Multiple travel modes
  Heterogeneous housing types
  Heterogeneous value of times
Results are echoed by the numerical studies with multiple OD pairs
Auto
r
s
Rail
……
Notes: Generally speaking, the analytical results is obtained for the case of simple one OD pair with multiple travel modes.
However, they are echoed by the numerical studies that implement the model for a network with multiple OD pairs.

## Slide 16: Properties
2
Property 1 (Residents)
  The travel cost of every HH group is monotonically increasing with headway and fare
  The changes of railway investment, e.g. headway or fare, do not result of changes in choice of housing types, and the locational benefit, e.g. individual/total CS, do not change
  The neutralizing effect on consumer surplus comes from transport externalities, where decrease in transport cost is absorbed by corresponding rent increases
  A regressive effect – High income gain more from transport service improvement
Auto
r
s
Rail
……
Notes: The observations from property 1 are standing from the residents’ point of view
Note that the unchanged consumer surplus for every income group in residential housing choice does not indicate that the overall impact of transport system changes (e.g. headway and fare) on residents of different income groups are the same. Actually, our previous research proved that residents with higher incomes and hence higher values of time benefit more from transport system improvements. Without going into the details of the proof, the intuition is that an improvement in transport infrastructure or reduction in transport cost will lead to an increase in housing rent, which is the same for all income groups and is equal to the travel cost as valued by the lowest income group . The same travel time saving would be valued higher by higher income groups due to their higher values of time. Therefore, for higher income groups, the increase in rental cost is smaller than the travel cost saving gained from transport infrastructure improvement. Hence, higher income groups will gain more from transport infrastructure improvements, or a regressive effect.

## Slide 17: Properties
2
Property 2 (Developer)
  The housing rents are monotonically decreasing with headway and fare
  If changing headway...
  there exists an optimal headway such that PS is maximized in a multi-modal network
    Headway ↑ Rail cost/revenue ↓ Housing cost/revenue →
Auto
r
s
Rail
……
Notes:   ON the other hand, from the developer point of view, the first obvious observation is that
  The most instersting observation is
  PS does not change with cp if rail is the only travel mode, since any railway fare increase (reduction) will be fully absorbed in the resultant housing rent by the same level of reduction (increase).
  both the railway revenue and cost are monotonically decreasing with the headway, while the housing revenue are monotonically decreasing with the headway

## Slide 18: Properties
2
Property 2 (Developer)
  If changing fare...
  PS is monotonically decreasing with fare in a multi-modal network
  Therefore developer will keep fare at a low level to maintain the PS at a high level, since the gain from housing sale offsets the reduction in fare revenue
  PS does not change with fare if rail is the only travel mode, fare increase fully absorbed in housing rent by the same level of reduction.
Auto
r
s
Rail
……
Notes:   PS does not change with cp if rail is the only travel mode, since any railway fare increase (reduction) will be fully absorbed in the resultant housing rent by the same level of reduction (increase).
  both the railway revenue and cost are monotonically decreasing with the headway, while the housing revenue are monotonically decreasing with the headway

## Slide 19: Sensitivity tests
2
One OD pair
Two travel modes
Two income groups
Two types of housing unit
Sensitivity tests
  Either fix Fare, and vary the number of Big units and Headway
  Or fix Headway, and vary the number of Big units and Fare
Auto
r
s
Rail
Notes: The above properties are also validated by sensitivity tests
Again, we assume an example of one OD…
Two sets of tests are conducted,

## Slide 20: Sensitivity tests
2
Vary Headway and % of Big units
Auto
r
s
Rail
Optimal investment
The total profit
Private developer
The social welfare
Government
Notes: These two figures show the resultant profit and social welfare when we altering
For the private developer, there exists an
If compared with other objective, for example, if the developer is the government who is to max the SW, then the test also give us the same optimal headway value, but it suggests to build more Big housing units.
Because Big gives more

## Slide 21: Sensitivity tests
2
Vary Fare and % of Big units
Auto
r
s
Rail
The total profit
Private developer
The social welfare
Government
Keep fare low
Notes: While on the other hand, the government may want both reducing and increasing so as to max SW

## Slide 22: Numerical example
3.
Notes: Because the overall proble is formulated as a MPEC, where normally it is hard to find and prove the existance of global optimal, we can stiil validate properties discovered under one OD case by numerical examples with multiple OD pairs.

## Slide 23: Numerical example
3
Numerical example
  With multiple OD pairs
Investing on
  Railway 2
  Zone 3 & 4
Scenarios
  Scenario 1 – Optimal joint investment
  Scenario 2 – Non-optimal (the same as old zones and Railway 1)
  Scenario 3 – Only optimizing headway and fare (the same as old zones)
CBD
2
1
4
3
2
1
4
3
6
5
R1_1
R1_2
R2_2
R2_1
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 24: Numerical example
3
Scenarios 1 – Optimal joint investment
  Investment decisions
    Lower headway on R2
    Larger proportion of Small units
    More units in Zone 4
  Residents’ choice
    Higher rail share in new zones
    Higher rail share in zone 4
CBD
2
1
4
3
2
1
4
3
6
5
R1_1
R1_2
R2_2
R2_1
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 25: Numerical example
3
Comparison among scenarios
  Optimal joint investment decisions (S1) is better not only in profit but also in consumer surplus and social welfare
Outcome indicators | Scenario 1 | Scenario 2 |  | Scenario 3 | 
Total travel time | 533 | 589 | -9.6% | 539 | -1.1%
Total consumer surplus | 1,340 | 1,237 | 8.3% | 1,238 | 8.3%
Housing profit | 313 | 212 | 47.2% | 225 | 39.0%
Railway profit | -127 | -150 | -15.0% | -123 | 3.7%
Total profit | 185 | 62 | 196.3% | 102 | 81.6%
Social welfare | 187 | 63 | 192.6% | 103 | 80.7%
Joint investment
Non-optimal
Optimal rail
Notes: Generally, the performances of Scenario A are better than the other two Scenarios in most aspects. The joint housing and railway investment scheme not only maximizes the developer’s total profit, but also results in higher consumer surplus and social welfare. In addition, it also reduces the total travel time. These results show that the joint housing and railway development performs better than separate housing and railway investment decisions, as it is more flexible in internalizing the tradeoff between housing and transport investments and revenues. The results also re-iterate that joint housing and railway development tends to improve the transport sysem performance on its own intiative, as evidenced in the total system travel time, which could be over-compensated by corresponding rental gains.

## Slide 26: Numerical example
3
Comparison among scenarios
  S1 is more flexible in finding tradeoff between rail and housing investment
  E.g. Private developer tends to improve the rail system performance on its own initiative
Outcome indicators | Scenario 1 | Scenario 2 |  | Scenario 3 | 
Total travel time | 533 | 589 | -9.6% | 539 | -1.1%
Total consumer surplus | 1,340 | 1,237 | 8.3% | 1,238 | 8.3%
Housing profit | 313 | 212 | 47.2% | 225 | 39.0%
Railway profit | -127 | -150 | -15.0% | -123 | 3.7%
Total profit | 185 | 62 | 196.3% | 102 | 81.6%
Social welfare | 187 | 63 | 192.6% | 103 | 80.7%
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 27: Conclusions
4.

## Slide 28: Conclusions
4
Developed a broader analytical framework of the integrated LUT system
Investigated the performance of a joint rail and housing investment strategy for a single profit oriented developer
Analytically studied the impact of such joint investment on the benefit distribution of different stakeholders under one OD condition
Numerical studies demonstrate the possibility of this joint investment on cross-subsidy between housing and rail investment
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 29: Future extensions
4
To extent this study into long-term framework so as to investigate the detailed cross-subsidy scheme over time
To investigate and compare the performances among various PPP modes
To investigate how to develop planning regulations on large-scale projects invested by private developers, e.g. TOD, so as to balance the interests of all the stakeholders
Notes: Objectives for instruction and expected results and/or skills developed from learning.

## Slide 30: Thank you