## Slide 1: Generation and Calibration of Transit Hyperpaths
Jan-Dirk SCHMÖCKER, Kyoto University
Hiroshi SHIMAMOTO, Kyoto University
Fumitaka, KURAUCHI, Gifu University
17-19 ISTTT20, JuLY 2013

## Slide 2: Transit Route choice models
Passengers often face complex route choice decisions and options to minimise their travel time.
Whereas drivers might change their route only when they encounter large delays, passengers are usually more flexible and react to small perturbations such as reversal in bus arrivals.
Frequency-based transit assignment models assume hence that passengers choose “optimal strategies”.

## Slide 3: Hyperpath Example: London tube
Assume a journey from Finchley Road to South Kensington.
(In case of unreliable arrivals) the optimal strategy might be to take from Finchley Rd “whichever line arrives first” and then to change at Baker Street or Green Park.

## Slide 4: Transit Assignment Literature
The attractive set is usually determined by a linear programming approach following Spiess and Florian (1989)
Since then the transit assignment literature has paid large emphasize on including congestion effects and, recently, effect of information on choice.
Much less attention to consideration of
  person-specific utilities, i.e. different weights for waiting vs. on-board time.
  Limiting complexity to “reasonable” size.

## Slide 5: However….
SP experiments (Kurauchi et al, 2012) and RP data (Fonzone et al, 2012) show that the hyperpath choice depends on person specific factors
  Sociodemographics
  PT experience
as well as experienced system performance
  Different hyperpath in crowded and/or unpunctual networks

## Slide 6: Discrete Choice Literature
Importance of choice calibration for drivers highlighted
“2-stage choice models” in which drivers first select a set of routes and then a route from this set by possibly different strategies
  “1-stage choice models” might also generate choice sets, but choice rules in both stages are similar.
Choice in both stages usually based on “utility maximisation”

## Slide 7: Objective of this paper
Define a DCM which explicitly considers two characteristics of optimal passenger behaviour in networks with uncertainty.
  Choice of bus set is based on utility, choice of bus not: “Take first arriving bus”
  The utility of a choice set is depending on the choice set size itself. The more buses the less the total expected waiting time: “A fast, infrequent bus alone is not attractive, but in combination with other bus lines it becomes attractive”
Illustrate how this model can be estimated with Smart card data.

## Slide 8: Logit Hyperpath Choice framework
Partly following the decision framework and notation of the “Generalised Logit” model by Swait (2001)
Probability that line i is chosen by person n at time t
Probability that choice set k is chosen by person n
Probability that line i is chosen among choice set Ck

## Slide 9: Line Choice
Probability to choose line i
where ai denotes the waiting time until line i arrives
Assuming that a) buses arrive with exponentially distributed headways and b) that passengers only know the service frequency this can be simplified to:
where fiτ denotes the service frequency of option i during departure time interval .
“Take first arriving bus”

## Slide 10: Line Set Choice
Logit model with choice probability determined by a time and person specific general cost or inclusive value Ikn associated with this nest / choice set:
Travel
time
Waiting time
Expected Transfers
Choice Set Size

## Slide 11: Line Set Choice (2)
Note that choice set utility is not the logsum of utility of options in nest but depends directly on the choice set size Cn and the options included in the nest:

## Slide 12: Model Properties
Therefore the model only collapses to standard MNL for special case
  all line frequencies fiτ take the same value
  all 2i-1 hyperpaths are possible
  tn = yn = 0 or ti and yi are the same for all options
In general our model is more sensitive to line frequencies due to the freq. based (“random”) lower choice model.

## Slide 13: Model Properties (2)
Consider choice between three lines.
  f1 = 5 t1 = 20 min
  f2 = 10 t2 = 25 min
  f3 = 15, t3 = 30 min

## Slide 14: Model Estimation
Combining lower and upper choice leads to
And maximum likelihood estimation to determine parameters an
where δis is 1 if sample s chooses option i and 0 otherwise.

## Slide 15: Model Estimation (2)
Gradient and Hessian of log likelihood function included in paper.
Due to the lower choice model Hessian takes a complex non-linear form.
We cannot establish that our objective function is concave and hence test convergence with different initialisation for our parameters.
Starting points appear to indeed influence our results, we report in the following results with best model fit.

## Slide 16: Calibration with smartcard data
Use of Smartcard data allows us to repeatedly observe the behaviour of individuals.
We use data from a local Japanese city for which we have two months records
  2,005,421 trip records made by 44,310 cards
Only some OD pairs for which passengers have a choice between lines. This limits our data significantly.

## Slide 17: Selected OD pairs
 | OD a |  |  | OD b |  |  |  |  |  | OD c | 
 | a1 | a2 | a3 | b1 | b2 | b3 | b4 | b5 | b6 | c1 | c2
Services per hour | 9-17 | 4 | 1-3 | 1-3 | 7-9 | 7-8 | 3-5 | 2-3 | 3-4 | 4-7 | 1-4
Operating hours | 5am-11pm | 6am -7am | 6am-8pm | 6m-8pm | 6am-11pm | 6am-11pm | 6am-10pm | 6am-7pm | 6am-11pm | 5am-11pm | 6am-9pm
Travel time (min) | 18-26 | 18 | 26-31 | 10-14 | 14-16 | 14-23 | 12-17 | 17-23 | 28 | 10-12 | 10-15

## Slide 18: Site characteristics
The card ID has been kept and individual behaviour can be tracked;
The whole city is covered only by the bus services and there is no rail service;
More than 70% of travellers use the smartcard data;
Boarding and alighting bus stops can be identified since travellers have to tap at boarding as well as alighting.
Service is schedule based. Therefore assumptions made on “frequency-based choice” possibly too simplistic.
Limited Network Complexity.

## Slide 19: User groups
Ticket type and “general behaviour” data allow us to distinguish four passenger groups (Kurauchi et al, 2012)
Do these groups use different hyperpaths?
User group | Characteristic of user group
Commuter | Hold commuter pass, travel often and mostly during weekday, include a large number of students.
Elderly | Hold elderly season pass, travel not often, mostly during day time, make almost no trips that include transfers.
Irregular | Passengers that fairly often make journeys that include transfers (23.6% of all journeys). Fairly few total journeys. Irregular OD patterns.
Other | Not passholders, fairly few total journeys, very few journeys that include transfers.

## Slide 20: Estimation results
 | OD a |  |  |  | OD b |  | OD c |  | All OD pairs | 
 | beta | t-value | beta | t-value | beta | t-value | beta | t-value | beta | t-value
Travel time t | -10.7 | -18.6 | -183.0 | -1062 | -43.9 | -57.1 | -65.8 | -441.3 | -87.6 | -218.6
Waiting time wn |  |  |  |  |  |  |  |  |  | 
Commuter | -10.8 | -6.83 | -62.7 | -351.1 | -3.58 | -5.98 | -1.48 | -3.74 | -33.8 | -219.4
Elderly |  |  | -75.7 | -862.0 | -34.0 | -523.8 | -26.8 | -420.2 | -46.6 | -427.3
Irregular |  |  | -69.7 | -173.0 | -0.59 | -0.07 | -1.20 | -1.59 | -34.1 | -35.1
Other |  |  | -79.6 | -474.9 | -2.99 | -1.16 | -18.5 | -124.65 | -48.1 | -256.2
Choice set size zn | -1.61 | -0.23 |  |  |  |  |  |  |  | 
sample size | 4033 |  | 4033 |  | 1589 |  | 958 |  | 6580 | 
2 | 0.51 |  | 0.51 |  | 0.15 |  | 0.31 |  | 0.27 | 
LL(0) | 2385.6 |  | 2385.6 |  | 2701.1 |  | 576.9 |  | 5663.5 | 
L* | 1177.7 |  | 1174.1 |  | 2305.5 |  | 394.9 |  | 4137.0 | 

## Slide 21: Estimation results (2)
Examples of Estimated Choice Set Probabilities
OD a, 6-7am | (a1) | (a2) | (a3) | (a1,a2) | (a1,a3) | (a2,a3) | (a1,a2,a3)
Commuter | 0.01 | 0.18 | 0.00 | 0.64 | 0.00 | 0.01 | 0.17
Elderly | 0.00 | 0.02 | 0.00 | 0.75 | 0.00 | 0.00 | 0.22
Irregular | 0.01 | 0.06 | 0.00 | 0.73 | 0.00 | 0.01 | 0.20
Other | 0.00 | 0.01 | 0.00 | 0.75 | 0.00 | 0.00 | 0.23
OD c, 7-8am | (c1) | (c2) | (c1,c2)
Commuter | 0.71 | 0.04 | 0.25
Elderly | 0.34 | 0.00 | 0.66
Irregular | 0.71 | 0.04 | 0.25
Other | 0.47 | 0.01 | 0.52

## Slide 22: Discussion
Travel time and waiting time parameters all have the expected sign.
Choice set size not significant, possibly due to strong correlation with waiting time.
Model fit varies significantly depending on the OD pair. With larger choice sets the model fit reduces as one would expect.
Group specific estimates of waiting in general lead to slightly better model fits.
Relative to on-board time older persons appear to dislike waiting time more than commuters and hence choose larger choice sets.

## Slide 23: sUMMARY
Route choice parameters in existing frequency based transit assignment models are mostly not calibrated. Smartcard data plus new methodologies allows doing so.
We propose a “hyperpath logit model” to consider specific transit characteristics in a discrete choice framework.
  Utility determines choice set
  Frequency determines line choice
Initial results with data from a Japanese city confirm that hyperpaths depend on person specific characteristics.

## Slide 24: Further work
Compare our results with that of other choice models.
Sensitivity to model assumptions such as service regularity (…limitation of our case study).
Consideration of panel effects and consideration of changing preferences during a day.
Repeating case study in more complex networks.

## Slide 25: Thank you! questions?
{schmoecker,shimamoto}
@trans.kuciv.kyoto-u.ac.jp
kurauchi@gifu-u.ac.jp