## Slide 1: Dynamic User Equilibrium in Public Transport Networks with Passenger Congestion and Hyperpaths
V. Trozzi 1, G. Gentile2, M. G. H. Bell3 , I. Kaparias4
1 CTS Imperial College London 2 DICEA Università La Sapienza Roma 3 Sydney University 4 City University London
Imperial College London
Università La Sapienza – Roma
Sydney University
City University London
Notes: This works deals with assignment in public transport networks and, more specifically, it extends hyperpath-based assignment to dynamic scenarios where overcrowding may occur.
Before introducing the structure of the model, let’s recall what is an hyperpath and how the models was developed.

## Slide 2: Hyperpath : what is this? Strategy on Transit Network
d
o
BUS STOP 2
BUS STOP 3
BUS STOP 1
2
1
2
1
1
3
3
4
1
3
3
4
Notes: What are travel strategies and why do we use them?
In densely connected urban networks with highly frequent services, passengers do not normally consider the lines’ timetable even when those are published.
Therefore, it is reasonable to assumed (and this is the usual assumption of Frequency-based models) that passengers make their travel choices considering average frequencies and in-vehicle travel times only.
However, when 2 or more lines with partially overlapping itineraries (common lines ) are available from the same stop, passengers do not know if it is better to board the first line approaching a bus stop or keep waiting for a more convenient service. What is the best option?

## Slide 3: Hyperpaths : why? Rational choice
d
o
BUS STOP 2
BUS STOP 3
BUS STOP 1
2
1
2
1
1
3
3
4
1
3
3
4
- Waiting - Variance
+ Riding + Walking =
+ Utility
Notes: Since the seminal works of Spiess and Florian (early eighties) it has been proved that, in this setting, the time to destination can be minimized by considering a bundle of potentially optimal itineraries, collectively referred to as “hyperpath” or “travel strategy”

## Slide 4: Dynamic Hyperpaths: queues of passengers at stops – capacity constraits
d
o
BUS STOP 2
BUS STOP 3
BUS STOP 1
2
1
2
1
1
3
3
4
1
3
3
4
Notes: This works extends the Frequency-Based transit assignment developed by Spiess and Florian to the case where recurring passenger congestion leads the formation and dispersion of First In First Out queues of passengers at the stop.

## Slide 5
Uncongested Network Assignment Map
Arc Performance Functions
Dynamic User Equilibrium model : fixed point problem
per destination
dynamic temporal profiles
cost
Notes: The proposed DUE, formulated as a fixed point problem, is obtained combining the supply and demand models or, equivalently, the Uncongested Network Assignment Map (which combines the results of the RCM and the NFPM) and APF.
In order to specify the Assignment models the following four components need to be specified:
the Stop Model (SM), which yields for any given attractive line set the probability of boarding each line as well as the expected waiting time, depending on: transit lines characteristics and on passenger congestion;
the Route Choice Model (RCM), which reflects the behaviour of a rational passenger travelling from an origin to a destination of the transit network for given arc performances (i.e. time-varying travel times and costs). The route choice in this paper is assumed deterministic and thus is modelled through a dynamic shortest hyperpath search;
the Network Flow Propagation Model (NFPM), which aims at finding time-varying arc flows that are consistent with the arc travel times for given route choices, but not consistent with line capacities. (this is the main difference between the NFPM and the Dynamic Network Loading Problem, where instead mutual consistence of flows and times through the APF is sought for given route choices);
the Arc Performance Function (APF), which yields the exit time at any given entry time for each arc, depending on the transit lines characteristics and the passenger flows over the network.

## Slide 6: 4. Network representation : supply vs demand
Notes: When the Network Flow Propagation Model determines the inflow on each arc of the network, Arc Performance functions are aplied to obtain the temporal profile of the exit time for any arc and entry time .
For pedestrian arcs, line arcs and waiting arcs, the value only depends on network characteristics, such as phyical lenght of the arcs, or supply characteristics, such as service frequency.
In this model it is assumed that the only Arc performance Function that also dpend on transit flows is the APF of queuing arcs.

## Slide 7: 4. Arc Performance Functions
The APF of each arc aA determines the temporal profile of exit time for any arc, given the entry time .
pedestrian arcs
line arcs
waiting arcs (this is for exp headways) frequency = vehicle flow propagation alng the line
Notes: When the Network Flow Propagation Model determines the inflow on each arc of the network, Arc Performance functions are aplied to obtain the temporal profile of the exit time for any arc and entry time .
For pedestrian arcs, line arcs and waiting arcs, the value only depends on network characteristics, such as phyical lenght of the arcs, or supply characteristics, such as service frequency.
In this model it is assumed that the only Arc performance Function that also dpend on transit flows is the APF of queuing arcs.

## Slide 8
Phase 1:
Queuing
Phase 2:
Waiting
Phase 1:
Queuing
Phase 2:
(uncongested) Waiting
4. Arc Performance Functions Bottleneck queue model
Notes: The contribution due to overcrowding is considered in the Performance Function of queuing arcs, which in turn depends on the current length of the queue at the stop by means of a Bottleneck Queuing Model with time-varying exit capacity.

## Slide 9
Available capacity
a’’
b
a’
τ
4. Arc Performance Functions propagation of available capacity
dwelling
riding
waiting
queuing
Notes: Description of the drawing: The square is a stop node – the hexagons are waiting node and the circles are boarding nodes
Dotted lines are queuing arcs – dashed lines are waiting arcs – full lines are (in-vehicle) line arcs
LAa is the line corresponding to the waiting arc WAa,
The, APF of this arc may be calculated using the equation in slide 6
However, for the corresponding queuing arc QAa, the exit time is obtained by applying a Dynamic Bottleneck Queuing Model with time-varying exit capacity.

## Slide 10
4. Arc Performance Functions bottleneck queue model
Time varying bottleneck
FIFO
The above Qout is different from that resulting from network propagation: this is not a DNL
they are the same only at the fixed point
Notes: The first equation of this slides solve the Performance Function of the Queuing arc QAa in the spirit of the Bottleneck Queuing Model :
The difference between the cumulative flow that has ENTERED the queuing arc (qIN) and the the cumulative flow that has LEFT the queuing arc (qOUT) is equal to the integral of the exit capacity of the queuing arc (which depends on the capacity available on board at the boarding time) during the queuing period.

## Slide 11
4. Arc Performance Functions numbur of arrivals to wait before boarding
While queuing some busses pass at the stop
Notes: The solution of the Bottleneck Model yields the total queuing time [, tQAa()] .
This value is used in turn to determine the congestion parameter, through the second equation:
The number of vehicles one passenger has to wait for is equal to the integral of the instantaneous frequency over the queuing time.
This congestion parameter is, then, used as an input of the Stop Model and Route Choice model to calculate the Erlang-distributed waiting time.
(This is shown in next transparency).
More specifcally the congestion parameter of the queuing arc is equal to the congestion parameter of the branch of the hyperarc (corresponding to the same line arc LAa) in the Hypergraph

## Slide 12: Hypergraph and Model Graph
WAa
QAa
LAa
a
LAa
Notes: It is very important to note here that:
the Stop Model and Route Choice Model are built with reference to a graphic structure (Hypergraph) where hyperarcs (those depicted in slide 6) are used to represent the total waiting +queuing time at the stop for the entire set of attractive lines (wh).
The Network Flow Propagation Model and the Arc Performance Functions consider a different graphic Structure (Model Graph), where proper waiting arcs are used to describe only the (uncongested) waiting for each line (last equation of slide 10) and only the «extra-waiting»time, or queuing time, that is due to overcorwding.
Two different graphic structures are chosen for describing the demand (RCM and SM) and the supply (NFPMand APF) because of the different phenomena that concern demand and supply.
On the one hand, on the demand-side, passengers do not perceive any difference between queuing and waiting times. Moreover, they tend to group together lines with partially overlapping itineraries (common lines) that share the same stop and consider them as a unique travel alternative, with its own total waiting (plus queuing) time and travel time upon boarding. The hyperarcs of the hypergraph HG are crucial to represent this combined waiting-plus-queuing time for a set of attractive lines considered together as a unique travel alternative.
On the supply-side, it is very important to separate the waiting from the queuing time in order to ensure consistency between the flow that leaves a queuing arc and the capacity available on the vehicle; consequently, in the model graph G it is chosen to distinguish waiting and queuing arcs. Moreover, because in the NFPM it is necessary to build a model with separate queues, combining the total waiting times of several lines through a hyperarc is not effective because it is difficult to represent the overtaking among passengers who want to board different sets of lines.

## Slide 13: 1. Stop model
BUS STOP 1
2
1
23
2
1
Assumption:
Board the first “attractive line” that becomes available.
2
23
1
23
2
1
Stop node 1
Line nodes
h = a1  a2
1
a2
a1
a2
a23
h = a2  a23
Notes: It is assumed that queuing passengers board whichever attractive line becomes available first
The Stop Model (SM), yields for any given attractive line set (or, equally, hyperarc h) the rate of passengers that will board each line (formally called conditional probabilities) and the expected waiting time (fore those who consider the hyperarc h) depending on:
transit lines characteristics (frequency and service regularity)
and on passenger congestion (how many vehicles of the same line do you need to wait before boarding?).
Some network notation: the set of attractive lines is graphically represented by an hyperarc (h), which has one tail node (the stop node) while its head includes as many line nodes as the line of the attractive set. Each branch pf the hyperarc (a) represents one attractive line.

## Slide 14: 1. Stop model
Notes: It is assumed that queuing passengers board whichever attractive line becomes available first
The Stop Model (SM), yields for any given attractive line set (or, equally, hyperarc h) the rate of passengers that will board each line (formally called conditional probabilities) and the expected waiting time (fore those who consider the hyperarc h) depending on:
transit lines characteristics (frequency and service regularity)
and on passenger congestion (how many vehicles of the same line do you need to wait before boarding?).
Some network notation: the set of attractive lines is graphically represented by an hyperarc (h), which has one tail node (the stop node) while its head includes as many line nodes as the line of the attractive set. Each branch pf the hyperarc (a) represents one attractive line.

## Slide 15: 2. Route Choice Model: Dynamic shortest hyperpath search
Waiting + Travel time after boarding
2
1
h = a1  a2
i
a2
a1
The Dynamic Shortest Hyperpath is solved recursively proceeding backwards from destination
Temporal layers: Chabini approach
For a stop node, the travel time to destination is :
Notes: In order to avoid explicit hyperpath enumeration, the formulation of the RCM can be seen as a recursive local choice that starts from the destination d and proceeds backwards to the origin(s). At each intermediate node i, passengers select the arc / hyperarc that minimizes the total travel time to d.
If the considered node is a stop node, then the travel time to destination is calculated using the equation shown in the slide.
Essential inputs of this equation are the results of the Stop Model (wh, pa|h).

## Slide 16: 2. Route Choice Model: Dynamic shortest hyperpath search
Erlang pdf for waiting times
Notes: Some more details about the equation:
The definition of: total waiting time (wh), conditional probability (pa|h) and conditional boarding time (ta|h(τ)= τ + wa|h(τ)) depend on the distribution of the total waiting time before boarding one specific line a.
When the usual assumtions about passenger and vehicle arrivals are accepted (passengers do not time their arrival at the stop with the service time-table annd vehicle arrivals follow a poisson distribution), but it further assumed that overcrowding leads to the formation dispersion of FIFO queues of passenger at the stop, then the waiting time before boarding line a is Erlang distributed with parametres:
φ: instantenous frequency of the line at the time of the day when the stop is reached
κ: congestion parameter of the line at the time of the day when the stop is reached (number of vehicle of the same line that one must wait before boarding)
The congestion parameter is the results of the Network Flow propagation Model and, then, Arc Performance Function on queuing arcs

## Slide 17: 2. Route Choice Model: Dynamic shortest hyperpath search
Erlang pdf for waiting times
Notes: Some more details about the equation:
The definition of: total waiting time (wh), conditional probability (pa|h) and conditional boarding time (ta|h(τ)= τ + wa|h(τ)) depend on the distribution of the total waiting time before boarding one specific line a.
When the usual assumtions about passenger and vehicle arrivals are accepted (passengers do not time their arrival at the stop with the service time-table annd vehicle arrivals follow a poisson distribution), but it further assumed that overcrowding leads to the formation dispersion of FIFO queues of passenger at the stop, then the waiting time before boarding line a is Erlang distributed with parametres:
φ: instantenous frequency of the line at the time of the day when the stop is reached
κ: congestion parameter of the line at the time of the day when the stop is reached (number of vehicle of the same line that one must wait before boarding)
The congestion parameter is the results of the Network Flow propagation Model and, then, Arc Performance Function on queuing arcs

## Slide 18: 3. Network flow propagation model
The flow propagates forward across the network, starting from the origin node(s).
When the intermediate node i is reached, the flow proceeds along its forward star proportionally to diversion probabilities:
i
a1 = 60%
a2 = 40%






Notes: Once the Route Choice Model is solved, for each arc and hyperarc of the network it is known its diversion probability, namely, the probability that the arc/hyperarc will be traversed to reach the destination.
This result is used in turns by the Network Flow Propagation Model to obtain the temporal profile of inflow for each arc.
The flow propagates forward across the network, starting from the origin node(s). Once the intermediate node i is reached, the flow propagates along its forward star, according to its arc diversion probabilities.
More specifically, the inflow on arc a∈FSi (forward star of i) at time  directed to destination dNC is given by the arc conditional probability ra,d() multiplied by the flow on node i at time .
In the example of the slide, the diversion probability of arc a1 is 60%, while for a2 it is 40%.
Finally, the flow on node i at time  (in the slide 5 passengers per minute) is given by the sum of: the flows that enter each arc of its backward star (BSi) at time , and reach i at time  ; and of the demand flow at the same time.

## Slide 19
Example Dynamic ‘forward effects’ on flows an queues
07:30
07:30
Dynamic ‘forward effects’: produced by what happened upstream in the network at an earlier time, on what happens downstream at a later time
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Line | Route section | Frequency (vehicles/min) | In-vehicle travel time (min) | Vehicle capacity (passengers)
2 | Stop 1 – Stop 4 | 1/6 | 25 | 50
1 | Stop 1 – Stop 2 | 1/6 | 7 | 50
1 | Stop 2 – Stop 3 | 1/6 | 6 | 50
3 | Stop 2 – Stop 3 | 1/15 | 4 | 50
3 | Stop 3 – Stop 4 | 1/15 | 4 | 50
4 | Stop 3 – Stop 4 | 1/3 | 10 | 25
Line 2 slow
Line 4 slow but frequent
Line 3 fast but infrequent
Origin | Destination | Demand (passengers/min)
1 | 4 | 5
2 | 4 | 7
3 | 4 | 7
Notes: This is the very well known network originally conceived by Spiess and Florian in 1989 of which characteristics (frequencies and in-vehicle travel times) shold be known.
Let’s study an example of dnamic assignment ot this network oer the analysis period [07:30 – 09:00]
Only one destination considered – Stop 4
Passengers who are at Stop 1 may board Line 2 or Line 1 and, then transfer at Stop3.
Passengers who are at Stop 2 may board Line 3 or Line 1 and, then, transfer at Stop 3
Passengers who are at Stop 3 may board Line 3 or Line 4.
Let’s now consider the most relevant dynamic effects that have been outlined in the example, starting with:
‘forward effects’ that the model can reproduce, i.e. effects produced by what happened upstream in the network at an earlier time of the day on what happens downstream at a later time.

## Slide 20
07:55
08:00
Example Dynamic ‘forward effects’
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Notes: From Stop 1: those who board Line 1 at 07:30 transfer at 07:55 at Stop 3.
From Stop 2: those who board Line 3 arrive at Stop 3 at 08:00 (they stay on board).

## Slide 21
Chart: Time of the day
| 0.3125 | 0.31944444444444398 | 0.32638888888888901 | 0.33333333333333298 | 0.34027777777777801 | 0.34722222222222199 | 0.35416666666666669 | 0.36111111111111099 | 0.36805555555555503 | 0.375
Line 3 | 3.3333 | 3.3333 | 3.3333 | 1.3345 | 1.3345 | 0 | 0 | 0 | 0 | 3.3333
Line 4 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333 | 8.3333
eQAa
Chart: kℓ(a)
| 0.3125 | 0.31944444444444398 | 0.32638888888888901 | 0.33333333333333298 | 0.34027777777777801 | 0.34722222222222199 | 0.35416666666666669 | 0.36111111111111099 | 0.36805555555555503 | 0.375
Line 3 | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 2 | 1 | 1
Line 4 | 1 | 1 | 1 | 2 | 3 | 3 | 2 | 2 | 2 | 1
07:55
08:00
Example Dynamic ‘forward effects’
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Notes: Because from 07:55 onwards some extra demand arrives at Stop 3 (namely, those who boarded Line 1 at Stop 1 at 07:30), Line 4 gets congested (κ >1) (Click here to show blue circle and harrow)
(Click here to hide blue circle and harrow) Afterwards, because those who boarded Line 3 at Stop 2 at 07:30 arrive at Stop 3 at 8:00, from this moment onwards the available capacity on Line 3 (eQAa) decreases and, therefore, from the following bus arrival (after 15 minutes – at 08:15) onwards congestion occurs also on Line 3 (κ >1) (Click here to show red circle and harrow)
‘Forward effect’: i.e. effects produced by what happened upstream in the network at an earlier time of the day (passengers boarding Line 1 at 07:30), on what happens downstream at a later time (queue of passengers, wishing to board Line 3, that occurs at stop 3 at 07:55).

## Slide 22
Example Dynamic ‘backward effects’ on route choices
Dynamic ‘backward effects’: produced by what is expected to happen downstream in the network at a later time on what happens upstream at an earlier time
08:12
08:44
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Notes: The analysis of Line 1 helps to clarify this concept. Line 1 never becomes congested at Stop 1 or 2. However, the expectation of a long queue at the transfer point (Stop 3) determines the decrease of its conditional probability at Stop 1 and Stop 2.

## Slide 23
08:12
Chart: Time of the day
| 0.3125 | 0.31944444444444398 | 0.32638888888888901 | 0.33333333333333298 | 0.34027777777777801 | 0.34722222222222199 | 0.35416666666666669 | 0.36111111111111099 | 0.36805555555555503 | 0.375
Line 3 | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 2 | 1 | 1
Line 4 | 1 | 1 | 1 | 2 | 3 | 3 | 2 | 2 | 2 | 1
Example Dynamic ‘backward effects’
08:44
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Notes: More specifically:
at 08:12 a long queue forms at Stop 3 for Line 3,
at 08:44 congestion on Line 3 will have dissipated.
Let’s now analyse the effect of the formation and dispersion of queues at Stop 3 on the route choice at Stop 1 and 2 and the conditional probability of Line 1

## Slide 24
08:12
Chart: Time of the day
| 0.3125 | 0.31944444444444398 | 0.32638888888888901 | 0.33333333333333298 | 0.34027777777777801 | 0.34722222222222199 | 0.35416666666666669 | 0.36111111111111099 | 0.36805555555555503 | 0.375
Line 3 | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 2 | 1 | 1
Line 4 | 1 | 1 | 1 | 2 | 3 | 3 | 2 | 2 | 2 | 1
Example Dynamic ‘backward effects’
Chart: pa*|h
| 0.3125 | 0.31944444444444398 | 0.32638888888888901 | 0.33333333333333298 | 0.34027777777777801 | 0.34722222222222199 | 0.35416666666666669 | 0.36111111111111099 | 0.36805555555555503 | 0.375
Line 1 | 0.49942 | 0.49942 | 0.49942 | 0 | 0 | 0 | 0.49942 | 0.49942 | 0.49942 | 0.49942
Line 2 | 0.49942 | 0.49942 | 0.49942 | 0.99971 | 0.99971 | 0.99971 | 0.49942 | 0.49942 | 0.49942 | 0.49942
08:44
07:53
08:25
Line 1
Line 1 and Line 3
Line 3 and Line 4
Line 2
1
4
3
2
Notes: Because of the queue that arises at 08:12 at Stop 3, since 07:53, the travel time upon boarding Line 1 from Stop 1 increases to such an extent that this line is excluded from the attractive set of Stop 1. (Click to hide green circles and harrows)
(Click to show orange circles and harrows) Line 1 is included again from 08:25 onwards, when the travel time upon boarding decreases again because, by the time Stop 3 will be reached (08:44), congestion on Line 3 will have dissipated.

## Slide 25
Example Dynamic change of line loadings
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
Line 1
Line 1
Line 4
Line 2
1
4
3
2
Line 3
Line 3
07:30
07:45
08:00
08:15
08:30
08:45
<20% capacity
20-39% capacity
40-59% capacity
60-79% capacity
80-100% capacity
Notes: Therefore, the application of such a dynamic model may produce a temporal profile of line loads (as those depicted in this slide) as well as a temporal profile of queuing, waiting times and diversion probabilities.

## Slide 26
- The model demonstrates the effects on route choice when congestion arises
- The approach allows for calculating congestion in a closed form (κ)
- Congestion is considered in the form of passengers FIFO queues
Conclusions:
Notes: Compare hyperpaths on the same slide.
Disregard numbers

## Slide 27: Dynamic User Equilibrium in Public Transport Networks with Passenger Congestion and Hyperpaths Thank you for your attention
Thank you for your attention!
Q&A
ValentinaTrozzi@tfl.gov.uk
Guido.Gentile@uniroma1.it
Michael.Bell@sydney.edu.au
Kaparias@city.ac.uk