## Slide 1: Sensitivity-based Uncertainty Analysis of a Combined Travel Demand Model
Chao Yang, Tongji University
Anthony Chen
Xiangdong Xu, Utah State University
S.C. Wong, University of Hong Kong
The 20th International Symposium on Transportation and Traffic Theory
July 17-19, 2013, the Netherlands
Notes: <number>

## Slide 2: Outline
<number>
Introduction
Travel Demand Forecasting Models
Sensitivity Analysis
Uncertainty Analysis
Numerical Examples
Conclusions

## Slide 3: Introduction
<number>
Transportation planning and project evaluation are both based on travel demand forecasting: subject to different types of uncertainties (Rasouli and Timmermans, 2012)
  Predicted socioeconomic inputs (i.e. population, employee)
  Calibrated parameters (i.e. dispersion parameter, BPR)
  Travel demand model itself (i.e., model structure & assumptions)
Without considering uncertainty in travel demand models, decision are likely to take on unnecessary risk and forecasts may be inaccurate and misleading (Zhao and Kockelman, 2002)

## Slide 4: Introduction (cont’d)
<number>
Most of the existing procedures in the travel demand forecasting are deterministic
Planners usually use point estimates of traffic forecasts in practice
There lacks a systematic methodology to conduct uncertainty analysis of a travel demand model (Rasouli and Timmermans, 2012)
Notes: Here deterministic refers to the output value, not the assumption on behavior error
<number>

## Slide 5: Literature Review
<number>
Waller et al. (2001) studied the impact of demand uncertainty on the results of traffic assignment model
Zhao and Kockelman (2002) addressed the uncertainty propagation of a sequential four-step procedure using Monte Carlo simulation
Pradhan and Kockelman (2002) & Krishnamurthy and Kockelman (2003) investigated the uncertainty propagation of an integrated land use-transportation model over time
Rasouli and Timmermans (2012) reviewed the uncertainty analysis in travel demand forecasting, including four-step models, discrete choice models, and activity-based models

## Slide 6: Typical Components of Uncertainty Analysis of a Model
<number>
Characterization of input/parameter uncertainty
  distribution characteristics (e.g., mean, variance) of input/parameter uncertainty
Uncertainty propagation
  output uncertainty resulting from input/parameter uncertainty
Characterization of output uncertainty
  mean, variance
  confidence level
  relationship between input/parameter & output

## Slide 7: Research Objective
<number>
To develop a systematic and computationally efficient network equilibrium approach for quantitative uncertainty analysis of a combined travel demand model (CTDM) using the analytical sensitivity-based method
  Modeling multi-dimensional demands and equilibrium flows on congested networks consistently
  Less computation than the sampling-based methods
  Uncertainties stemming from input data and model parameters can be treated separately, so that the individual and collective effects of uncertainty on the outputs can be clearly quantified
Notes: Our approach has the following three key features

## Slide 8: Travel Demand Forecasting Models
<number>
Oppenheim (1995) proposed a combined travel demand model (CTDM), which combines the travel-destination-mode-route choice based on the random utility theory
  A viable avenue with behavioral consistency for modeling and predicting multi-dimensional demands and equilibrium flows
Notes: Different rationales along with different assumptions (e.g., Gravity model in trip distribution step, Logit model in modal split step, and UE model in traffic assignment step)
no guarantee that it will always converge to give stable and accurate results

## Slide 9: Combined Travel Demand Model
<number>
Travel
Destination
Mode
Route
Notes: Hierarchical choice structure that can be modeled by nest logit.
<number>

## Slide 10: Oppenheim’s Model (1995)
<number>
Conservation constraints
Direct utility of route-mode-destination-travel choices
Entropy terms of route, mode, destination choices
Entropy terms of travel and no travel choices
Unique Solution!
Oppenheim, N. (1995) Urban Travel Demand Modeling, John Wiley & Sons.
Notes: Conceptually, this objective function integrates the utility maximization of individual travelers and the congestion effect (i.e., multiple travelers) by combining multi-dimensional discrete choice concept into the network equilibrium problem.
To sum up, the motivations of adopting the CTDM in the uncertainty analysis include: (1) a single unifying rationale (i.e., utility maximization theory), and (2) elegant closed-form probability expressions for all travel choice dimensions and a unique solution to the CTDM formulation.

## Slide 11: Sensitivity Analysis
<number>
Follow the approach of Yang and Bell (2007), we can prove that M is invertible
Notes: Sensitivity analysis is an effective way to quantitatively analyze the behavior of demand and flow pattern with respect to the perturbations of network characteristics.
E refers to perturbation; M is Hessian matrix of Lagrangian function of CTDM; N is gradient vector of Lagrangian function. Y is vector of model outputs and lagrangian multiplier.

## Slide 12: Sensitivity Analysis
<number>
Estimated solution using the first-order Taylor series approximation
Matrix manipulation and differential chain rule
Notes: dt/de is the apparent derivatives, and t/e is true partial derivatives.
<number>

## Slide 13: Propagation of Uncertainties
<number>
Two possible approaches:
Sampling-based method
  high computational effort
  non-reproducibility
  Linear regression of input/output
Analytical sensitivity-based method
Notes: <number>

## Slide 14: Uncertainty Analysis
<number>
Variance-covariance matrix of outputs
Confidence intervals of outputs (normality)
Covariance of outputs and inputs
Correlation of output i & input j (critical inputs)
Given
Sensitivity
An analytical method based on sensitivity analysis of CTDM

## Slide 15: Remarks
For non-separable link cost with asymmetric interaction, CTDM can be formulated as VI, and sensitivity analysis for VI could be adopted
Sampling-based methods and sensitivity based analytical method is a tradeoff between information richness and computational burden
<number>

## Slide 16: Numerical Results
<number>
2 modes: car (c) and transit (t)
# of potential travelers: N1=200
Attractiveness: h1=5.0, h14=3.5, h15=3.8, h14c=3.5, h14t=3.6, h15c=3.8, h15t=3.4
Parameters associated with route, mode, destination and travel choices

## Slide 17: Selected Outputs for Analysis
<number>
T1: production from zone 1
T10: number of non-travelers from zone 1
T14: O-D demand from zone 1 to zone 4
T14c, T14t: O-D demands from zone 1 to zone 4 by car and transit
T14c1, T14c2, T14c3: flows on three routes b/t O-D (1, 4) using car
v1c, v1t: flows on link 1 in car and transit networks
TTT: total travel time (TTT)
TVM: total vehicle miles (TVM) traveled

## Slide 18: Multi-Dimensional Equilibrium Solution
<number>
Choice probability and expected received utility
Notes: the equilibrium solution pattern satisfies the logit-type choice probability

## Slide 19: Multi-Dimensional Equilibrium Solution
<number>
Multi-dimensional equilibrium demand
Consistent with the tree structure (i.e., traveler’s expected received utility at the corresponding choice stage)

## Slide 20: Sensitivity Analysis Results
<number>
Derivatives of outputs with respect to inputs
link capacities in car network
Conservation
Significance
Notes: Sensitivity conservation
N1 is significant on T1,T10, OD demand and TTT, TVM
Link capacity of car network has more influence on car OD.

## Slide 21: Sensitivity Analysis Results
<number>
Derivatives of outputs with respect to parameters
attractiveness
link cost functions
choices
Notes: need to put more efforts and resources to enhance the calibration and validation of parameters βt, βd, αc and αt

## Slide 22: Estimated and Exact Solutions for Perturbed Input and Parameter
<number>
Estimate the equilibrium solution without the need to resolve the CTDM
N1 and βt have a large derivative value

## Slide 23: Uncertainty from Inputs
<number>
Coefficient of variation (CoV) of inputs = 0.30
Notes: Assume normal and independent of input
<number>

## Slide 24: Correlation of Outputs with Inputs
<number>
Identify critical inputs relative to output uncertainty by the correlation of inputs and outputs
Notes: relationship between the model inputs and outputs, regardless of whether they are dependent or not, and how positively or negatively correlated if they are dependent

## Slide 25: Uncertainty from Parameters
<number>
Coefficient of variation (CoV) of paramters= 0.30
Notes: The impact of parameter uncertainty on output uncertainty is generally higher than that of input uncertainty.
to improve the confidence level of the estimated outputs of each choice step, improving the accuracy of parameter estimation is more effective than that of improving input estimation.

## Slide 26: Benefit of Improving Parameter Estimation
<number>
Notes: when the accuracy of parameter estimation increases, the accuracy of output estimation will also increase

## Slide 27: Correlation of Outputs with Parameters
<number>
Notes: The correlation matrix can help the model users to identify the critical parameters for improvement.

## Slide 28: Uncertainty from Both Input and Parameter Uncertainty
<number>
Outputs uncertainty (SD and CoV) from both inputs and parameters uncertainty is not simply the sum of individual uncertainties
Notes: combined impact of inputs and parameters uncertainty on the outputs uncertainty
TVM seems to be a more reliable system performance metric given the uncertainty of both inputs and parameters.

## Slide 29: Output Uncertainty at Each Travel Choice Step
<number>
equilibrium nature of traffic assignment

## Slide 30: Concluding Remarks
<number>
Proposed a systematic analytical sensitivity-based approach for the uncertainty analysis of a CTDM
Required significantly less computational efforts than the sampling-based methods
Quantified the individual & collective effects of input and parameter uncertainties on outputs
Can estimate the possible benefits of improving the parameter accuracy
Notes: This information enables planners to effectively allocate the limited resources for input data collection and parameter estimation of key variables.

## Slide 31: Thank You!
<number>
Acknowledgements
The authors are grateful to three anonymous referees and especially to Prof. Hai Yang for valuable comments on the sensitivity analysis formulation.
This research was supported by the Oriental Scholar Professorship Program sponsored by the Shanghai Ministry of Education in China to Tongji University, National Natural Science Foundation of China (71171147), Fundamental Research Funds for the Central Universities, and the China Scholarship Council.